## Slide 1: Carry Look-Ahead Adder
Jheel Makhijani
Drashti Khatri

## Slide 2: Why CLA?
In RCA, if number of bits increases, propagation delay increases. There is carry dependency in RCA.
Hence, CLA is used to eliminate propagation delay.

## Slide 3: Pi = Ai ⊕ Bi Gi = Ai · Bi
Carry Propagator
Carry Generator

## Slide 4: How it Works
Sumi = Pi ⊕ Ci
Ci+1 = Gi + ( Pi · Ci)
C1 = G0 + P0 · C0
C2 = G1 + P1 · C1 = G1 + P1 · G0 + P1 · P0 · C0
C3 = G2 + P2 · C2 = G2 P2 · G1 + P2 · P1 · G0 + P2 · P1 · P0 · C0
C4 = G3 + P3 · C3 = G3 P3 · G2 P3 · P2 · G1 + P3 · P2 · P1 · G0 + P3 · P2 · P1 · P0 · C0

## Slide 5: Advantage Drawback
It does not need to wait till the previous stage generates the carry. It can generate carry for each full adder simultaneously, hence it is faster as compared to the ripple carry adder.
Requires complex hardware to generate the carry based on input signals and the complexity grows with an increasing number of bits.

## Slide 6: module CarryLookAheadAdder(A,B,Cin,S,Cout); input [3:0]A, B,; input Cin; output [3:0] S; output Cout; wire [3:0] Ci; assign Ci[0] = Cin; assign Ci[1] = (A[0] & B[0]) | ((A[0]^B[0]) & Ci[0]); assign Ci[2] = (A[1] & B[1]) | ((A[1]^B[1]) & ((A[0] & B[0]) | ((A[0]^B[0]) & Ci[0]))); assign Ci[3] = (A[2] & B[2]) | ((A[2]^B[2]) & ((A[1] & B[1]) | ((A[1]^B[1]) & ((A[0] & B[0]) | ((A[0]^B[0]) & Ci[0]))))); assign Cout = (A[3] & B[3]) | ((A[3]^B[3]) & ((A[2] & B[2]) | ((A[2]^B[2]) & ((A[1] & B[1]) | ((A[1]^B[1]) & ((A[0] & B[0]) | ((A[0]^B[0]) & Ci[0]))))))); assign S = A^B^Ci; endmodule

## Slide 7
RTL Schematic

## Slide 8: `timescale 1ns / 1ps module CLA_tb; reg [3:0] A,B; reg Cin; wire [3:0] S; wire Cout; integer i,j; CarryLookAheadAdder uut (.A(A), .B(B), .Cin(Cin), .S(S), .Cout(Cout)); initial begin A = 0; B = 0; Cin = 1; #100; for(i=0;i<=15;i=i+1) begin A=i; #5; for(j=0;j<=15;j=j+1) begin B=j; #5; $display("A=%b, B=%b, Cin=%b, S=%b, Cout=%b",A,B,Cin,S,Cout); end end #5 $finish; end endmodule

## Slide 9: Simulation